## Slide 1: ALU Design using Verilog
Lab 3
By: Er. Shiva Raj Luitel

## Slide 2: Objective
To implement ALU using Verilog HDL.

## Slide 3: ALU
An arithmetic logic unit (ALU) is a digital circuit used to perform arithmetic and logical operations. It represents the fundamental component of a computer's CPU. Modern processors contain very powerful and complex ALUs. In addition to ALUs, modern CPUs contain a control unit (CU).
An ALU performs basic arithmetic and logic operations. Examples of arithmetic operations are addition, subtraction, multiplication, and division. Examples of logical operations are comparisons of values such as NOT, AND, and OR

## Slide 4: ALU Operation Table

## Slide 5: Verilog code
module ALU (a, b, s, yout, cf);
input [3:0] a;
wire [3:0] a;
input [3:0] b;
wire [3:0] b;
input [2:0] s;
wire [2:0] s;
output [3:0] yout;
reg [3:0] yout;
output cf;
reg cf;
reg [4:0] temp;
always @ ( a,b,s )
begin
if ( s == 3'b000)
begin
temp = {0,a} + {0,b};
yout = temp [3:0];
cf = temp [4];
end
else if ( s == 3'b001)
begin
temp = {0,a} - {0,b};
yout = temp [3:0];
cf = temp [4];
end
else if ( s == 3'b010)
begin
temp = {0,a} + 5'b00001;
yout = temp [3:0];
cf = temp [4];
end
else if ( s == 3'b011)
begin
temp = {0,a} - 5'b00001;
yout = temp [3:0];
cf = temp [4];
end
else if ( s == 3'b100)
begin
temp = a | b;
yout = temp [3:0];
cf = temp [4];
end
else if ( s == 3'b101)
begin
temp = a & b;
yout = temp [3:0];
cf = temp [4];
end
else if ( s == 3'b110)
begin
temp = a ^ b;
yout = temp [3:0];
cf = temp [4];
end
else if (s == 3'b111)
begin
temp = ~a;
yout = temp [3:0];
cf = temp [4];
end
end
endmodule

## Slide 6: RTL and technology schemetic

## Slide 7: Test Fixture
initial begin
a = 0;
b = 0;
s = 0;
#100;
a=5;
b=6;
s=1;
#100;
a=5;
b=6;
s=2;
#100;
a=5;
b=6;
s=3;
#100;
a=5;
b=6;
s=4;
#100;
end
endmodule

## Slide 9: Verilog Coding
module alu(
input [7:0] A,B, // ALU 8-bit Inputs
input [3:0] ALU_Sel,// ALU Selection
output [7:0] ALU_Out, // ALU 8-bit Output
output CarryOut // Carry Out Flag
);
reg [7:0] ALU_Result;
wire [8:0] tmp;
assign ALU_Out = ALU_Result; // ALU out
assign tmp = {1'b0,A} + {1'b0,B};
assign CarryOut = tmp[8]; // Carryout flag

## Slide 10: Contd…
always @(*)
begin
case(ALU_Sel)
4'b0000: // Addition
ALU_Result = A + B ;
4'b0001: // Subtraction
ALU_Result = A - B ;
4'b0010: // Multiplication
ALU_Result = A * B;
4'b0100: // Logical shift left
ALU_Result = A<<1;
4'b0101: // Logical shift right
ALU_Result = A>>1;
4'b0110: // Rotate left
ALU_Result = {A[6:0],A[7]};
4'b0111: // Rotate right
ALU_Result = {A[0],A[7:1]};
4'b1000: // Logical and
ALU_Result = A & B;
4'b1001: // Logical or
ALU_Result = A | B;
4'b1010: // Logical xor
ALU_Result = A ^ B;
4'b1011: // Logical nor
ALU_Result = ~(A | B);
4'b1100: // Logical nand
ALU_Result = ~(A & B);
4'b1101: // Logical xnor
ALU_Result = ~(A ^ B);
4'b1110: // Greatercomparison
ALU_Result = (A>B)?8'd1:8'd0 ;
4'b1111: // Equal comparison
ALU_Result =(A==B)?8'd1:8'd0 ;
default: ALU_Result = A + B ;
endcase
end
endmodule

## Slide 11: Test fixture
initial begin
A = 8'h0A;
B = 8'h02;
ALU_Sel = 4'h0;
for (i=0;i<=15;i=i+1)
begin
ALU_Sel = ALU_Sel + 4'h01;
#10;
end;
A = 8'hF6;
B = 8'h0A;
end

## Slide 12: Observation
RTL and Timing diagram

## Slide 13: Discussion and conclusion